## Slide 1: RAF BENSON & RAF ODIHAM RADAR
Future Operating Model Aircrew Brief
OFFICIAL - SENSITIVE

## Slide 2
Supervisor
TC (JAC) (Sup)
Established as required iaw Local Orders and responsible for oversight in conjunction with the Allocator.
Landline C/S: JAC Supervisor
Allocator
TC (JAC) (Alloc)
Established permanently with authority to control at low intensity, responsible for oversight alongside landline and frequency monitoring.
Landline C/S: JAC Supervisor / JAC Allocator
Voice C/S: Southern Mil Allocator
BEN App
TC (BO) (RA) & TC (BO) (Dir)
Responsible for IFR Departures and Recoveries at BEN.
Landline & Voice C/S: Benson Approach
ODI App
TC (OI) (RA) & TC (OI) (Dir)
Responsible for IFR Departures and Recoveries at ODI.
Landline & Voice C/S: Odiham Approach
Radar
TC (JAC) (Rad)
Established as a single or multiple positions through task management, responsible for VFR Departures, GH, VFR Recoveries, IFR transits and MATZ crossings for both BEN and ODI.
Landline C/S: JAC Radar (1 / 2 / 3)
Voice C/S: Southern Mil
Talkdown
TC (BO) (SRA)
Established as a single underpinned with individual endorsements, responsible for SRA provision to BEN and ODI.
Landline & Voice C/S: ODI / BEN Talkdown
TC (OI) (SRA)
Operating model: new

## Slide 3
Frequencies
Freq position | Voice Callsign | STUD | Frequency | Notes
Southern Mil (ICF*) | Southern Mil Allocator | #4 | 245.625 | 
Southern Mil (ICF*) (VHF) | Southern Mil Allocator | #14 | 134.035 | 
Southern Mil Radar | Southern Mil | #3 | 275.450 | Previously ‘BEN Zone’
Southern Mil Radar (VHF) | Southern Mil | #19 | 120.905 | Previously ‘BEN Zone’
Southern Mil Radar | Southern Mil | #13 | 343.525 | Previously ‘ODI Zone’
Odiham Approach | Odiham Approach | #5 | 313.375 | 
Odiham Approach (VHF) | Odiham Approach | #6 | 131.305 | 
Benson Approach | Benson Approach | #15 | 342.100 | 
Benson Approach (VHF) | Benson Approach | #16 | 136.455 | 
Inbound to Benson or Odiham:
Utilise Southern Mil (ICF) –
134.035/245.625
Traffic will either maintain this frequency or be handed to BEN or ODI Approach
MATZ crossing and Transits of Benson or Odiham:
Utilise Southern Mil Radar –
120.905/275.450/343.525
*ICF – Initial Contact Frequency